## Slide 1: RISC-V Super-Scalar Out-of-Order Simulator
Finn Cooper – sd22404

## Slide 3
RV32I base integer instructions (majority)
  no ebreak/ecall/fence/csr
RV32M multiply/divide extension (full)
RV32F floating-point extension (majority)
  no flags/fcsr
RV32V vector extension (limited)
  LMUL 1, ELEN 32, VLEN 128/256/512
Seven-stage pipeline:
  fetch -> decode -> dispatch -> issue -> execute -> writeback -> commit
32-wide integer, float and vector register files
Out-of-order issue via reservation stations
In-order commit via 64-wide re-order buffer
Renaming via tag-based register alias tables
Configurable fetch/issue/commit widths
Configurable number of execution units
Multiple branch prediction policies:
  static taken
  static not taken
  static backward taken forward not taken
  dynamic two-bit saturating counter
Relaxed memory policy:
  non-overlapping loads bypass pending older stores
  overlapping loads have older stores forwarded at byte level
Interactive terminal UI
  step/run, headless mode
  registers, stack
Stack handling, function calls
Configurable cycle exec units

## Slide 4: Benchmarks
dot product
fibonacci
gaussian
matmul
quicksort
saxpy

## Slide 5: Experiment One – Pipeline Width
Hypothesis
Increasing pipeline width will lead to increased IPC across all benchmarks.
Experiment
Results
...

## Slide 6: Experiment Two – Branch Prediction Policies
Hypothesis
Increasing pipeline width will lead to increased IPC across all benchmarks.
Experiment
Results
...

## Slide 7: Experiment Three - Vectorisation
Hypothesis
Increasing the maximum vector length will decrease the number of cycles taken to execute SIMD benchmarks and therefore speed up execution compared the baseline non-vectorised version.
Experiment
The four SIMD-friendly benchmarks were executed with the same configuration besides the maximum vector length. The number of cycles taken to complete.
Results
All benchmarks show a similar decrease of about 10x in the number of cycles taken.