## Slide 1: RISC-V Pipelined Scalar Simulator
Finn Cooper – sd22404

## Slide 2: Microarchitecture

## Slide 3: Features
RV32im – implemented base unprivileged ISA with multiply extension
  Omitted ‘FENCE’ instructions, ECALL and EBREAK
5-stage pipeline
  Fetch, Decode, Execute, Memory Access, Writeback
  Operand Forwarding - stall only on load-use hazard if enabled
  Otherwise stall for all data hazards
  Pipeline flushing for control hazards
ELF file parsing with ‘elfio’ library
  Compiles C programs to RISC-V ELF binary with riscv64-unknown-elf-gcc
TUI interface
  Displays disassembly with instruction pointer for each pipeline stage
  Displays registers and stack, with highlighted changes since the last cycle

## Slide 4: Planned Improvements
Superscalar execution
  Begin with 2-wide, later configurable
Branch prediction
  Support for different dynamic algorithms
Reservation stations, reorder buffer & register renaming
  Following Tomasulo’s algorithm
Support for 64-bit instructions (RV64)
Support for floating point instructions (“F” extension)
Support for vector instructions (“V” extension)

## Slide 5: Planned Experiments & Benchmarks
Performance of branch prediction algorithms
  Compare dynamic algorithms (e.g. one and two-bit saturation counters)
  Compare best dynamic to static not-taken and static taken
Performance uplift of vector operations
  Compare performance across benchmarks with vector extension enabled and disabled
Evaluation of pipeline width across benchmarks
Benchmarks
  Sorting algorithms
  Livermore Loops
  Recursive algorithms